## Slide 1
in collaboration with The National Centralized Repository for Alzheimer’s Disease and Related Dementias (NCRAD)
Blood-Based Biospecimen Training Slides

## Slide 2: Contact Information
Questions?
Please contact NCRAD Coordinator at:
  Phone: 317-274-7890
  CRC email: dlkeys@iupui.edu
  Back-up email: alzstudy@iu.edu
  Website: www.ncrad.org

## Slide 3: Training Overview:
Blood-Based Collection Schedule
Kit Request Module
Specimen Labels
Handling/Processing Study Specimens
Sample Shipping
NCRAD Website
Questions?

## Slide 4: HEAD Biospecimen Collection Schedule
Specimen Type | Baseline Visit | 18 Month Visit
**Whole Blood for RNA | X | X
Serum | X | 
Plasma | ***X | *X
DNA | X | X
Whole Blood for Banking | X | X
**2.5 ml PAXgeneTM Blood RNA Tube
*6 x 10ml EDTA tubes are collected
***5 x 10ml EDTA tubes are collected
Notes: Whole blood is collected in three types of tubes (10ml Serum-Separator/SST Tube, 10ml lavender-top EDTA tube and 6ml EDTA tube). The 10ml red-top serum separator tube is processed locally into serum and then aliquoted, frozen at the study site and shipped to NCRAD. The 10ml EDTA tubes are processed locally into plasma and buffy coat fractions. They are then aliquoted, frozen at the study site, and shipped to NCRAD. The 6ml EDTA tube is frozen locally without further processing and shipped to NCRAD.

## Slide 5: Kit Request Module
https://kits.iu.edu/head

## Slide 6: Kit Request Module
An initial stock of kits will be delivered prior to the designated site specific start date.
Kits and individual supplies are available to order:
  Blood-Based Kit
  Frozen Blood Shipping Supply Kit
  Blood-Based Supplemental Supply Kit (1 only at study start up)
  Individual Supplies

## Slide 7: NCRAD Kit Request Module
Choose your site from the drop- down list
The coordinator name and contact information will appear
Verify that this information is accurate, correct if necessary

## Slide 8: Kits Available
Pending link when HEAD added to NCRAD.ORG

## Slide 9: Study Visit Kits
Indicate the quantity needed of each kit
Once selected, kit components of the chosen kit will appear at the bottom of the screen (Pictured)
Click “Submit” to turn in your request.
The IU staff will notify you that your request has been received and address any issues.
**Note: You can order more than one type of kit in a single kit request**
Pending link when HEAD added to NCRAD.ORG

## Slide 10: NCRAD Kit Request Module: When It Must be Used
Each site will be responsible for ordering kits (labels included) and maintaining supplies on site for scheduled participants
To order, sites will use the Indiana University online kit ordering module: https://kits.iu.edu/head
Allow a minimum of 2-3 weeks for your order to be processed and delivered.

## Slide 11: Specimen Labels

## Slide 12: Label Type Summary
Kit Number Labels
HEAD ID Labels
Collection Tube Labels
  Differ by specimen type
Cryovial Labels

## Slide 13: Kit Number Labels
Used to track patient samples and provide quality assurance
Will be placed on the following locations:
  Biological Sample and Shipment Notification Form
  Outside cryobox that houses aliquot tubes during storage and shipment
  Provided by NCRAD in the kits

## Slide 14: HEAD ID Label
Subjects will be identified by their HEAD ID
The HEAD ID may only be available shortly before the visit
Sites will be responsible for handwriting this onto the provided labels
  Must use Fine point permanent marker

## Slide 15: Collection Tube Labels
Specimen Barcode (assigned by NCRAD)
Study Name
Sample Type
Kit # (assigned by NCRAD) unique to the subject and visit

## Slide 16: Collection Tubes - Blood
All collection tubes will have two labels
  The Collection Tube Labels
  The handwritten HEAD ID Label
Label 1: Collection Tube Label
Label 2: HEAD ID Label
Collection/Aliquot
tube label *place barcode near top
HEAD ID label
Buffy Coat

## Slide 17: Cryovial Tube Labels – Serum, Plasma and Buffy Coat
Cryovial tube label only
Please don’t cover barcode on tube with label!
Notes: Need new photo of micronic

## Slide 18: Labeling Biologic Samples
Please...
Label all collection and aliquot tubes before cooling, collecting, processing or freezing samples.
Label only 1 subject’s tubes at a time to avoid mix-ups.
Wrap the label around the tube horizontally. Label position is important for all tube types.
Make sure the label is completely adhered by rolling between your fingers.
Notes: Is this accurate for the micronic tubes? ADD EXAMPLE OF collection tube as well!

## Slide 19: Handling/Processing Study Specimens

## Slide 20: Site Required Equipment
Blood Collection/Safety Equipment
PPE
  Lab Coat, Safety Glasses
Tourniquet
Alcohol Prep Pad
Gauze Pad
Butterfly Needles
Bandage
Sharps Bin and Lid
Processing/Storage Equipment
Centrifuge capable of ≥2000 rcf with refrigeration to 4⁰C
-80⁰C Freezer
Wet Ice Bucket
Notes: Confirm if all needed for this study

## Slide 21: Sample Collection - Blood
Draw Tube Order | Tube Type | Number of Tubes Drawn | Tube Image
1 | PAXgene™ Tube for RNA | 1 | 
2 | Serum (Red-Top) Tube (10 ml) | 1 | 
3 | EDTA (Lavender-Top) Tube (10ml) | x 5 (baseline) X 6 (18M) | 
4 | EDTA (Lavender-Top) Tube (6 ml) | 1 | 
Notes: UPDATE?

## Slide 22: Aliquot Cap Colors
Cap Color | Sample Type
Red Cap | Serum
Purple Cap | Plasma
Blue Cap | Plasma Residual (<1.5ml) (Document Specimen Number and Volume of Residual Aliquot on Sample Form)
Gray Cap | Buffy Coat
Purple Cap (Plasma)
Gray Cap (Buffy Coat)
Blue
Cap (Residual)
Red Cap (Serum)

## Slide 24
Baseline Visit Only

## Slide 25
Serum Tube (Serum Collection)
Serum Tube (unfilled)
** Please note: After standing at room temperature for 30 minutes, blood will be clotted and immobile**
Serum Tube (after centrifuge)

## Slide 26
Baseline Visit Only

## Slide 27: EDTA Tube (Plasma Collection)
Plasma Aliquots
(up to 17 for baseline visit)
Close up view of 2.0 ml cryovial
Notes: UPDATED PHOTOS IN NEW CRYOBOX FOR MICRONICS?

## Slide 28: EDTA Tube (Buffy Coat Collection)
Important Note:
Buffy Coat aliquots will be distinguished from the plasma aliquots through a gray cap.

## Slide 29
18M Visit Only

## Slide 30: EDTA Tube (Plasma Collection)
Plasma Aliquots
(up to 20 for 18M visit)
Close up view of 2.0 ml cryovial
Notes: UPDATED PHOTOS IN NEW CRYOBOX FOR MICRONICS?

## Slide 31: EDTA Tube (Buffy Coat Collection)
Important Note:
Buffy Coat aliquots will be distinguished from the plasma aliquots through a gray cap.

## Slide 33: Sample Shipping

## Slide 34: Blood Sample Shipment Summary
Sample Type | Tube Type | Tubes to NCRAD | Ship
Whole blood for transcriptome analysis | PAXgene™ Blood RNA Collection Tube (2.5 ml) for RNA | 1 | Frozen
Whole blood for isolation for serum | SERUM: 2.0 ml cryovials with red cap (residual volume placed in 2.0 ml cryovial with blue cap) | Up to 4 (baseline) | Frozen
Whole blood for isolation of plasma & buffy coat (for DNA extraction) | PLASMA: 2.0 ml cryovials with purple cap (residual volume placed in 2.0 ml cryovial with blue cap) | Up to 17 (baseline) Up to 21 (18M) | Frozen
 | BUFFY COAT: 2.0 ml cryovial | 5 (baseline) 6 (18M) | Frozen
Whole blood for future analysis | EDTA (Lavender-Top) Blood Collection Tube (6 ml) | 1 | Frozen

## Slide 35: Frozen Sample Shipping
Ship Monday-Wednesday Only
  Plasma
  Buffy Coat
  Serum
  Whole Blood for RNA
Hold packaged samples in a -80°C freezer until pickup.
Batch Samples together
  5 cryoboxes
  Batch shipping should be performed quarterly or as a full shipment of specimens accumulates, whichever is sooner.
Notes: Which samples are sent frozen vs ambient??

## Slide 36: Frozen Shipping - Cryoboxes
Place cryobox in one Biohazard Bag.
Place frozen RNA and EDTA (6ml) tubes (when applicable) in separate bubble wrap tube sleeves
Notes: Updated photos: pending decision on micronic cryobox or original cryobox

## Slide 37: Shipping Frozen Samples
Schedule UPS
Send Biological Sample and Shipment Notification Form to IU (US) ahead of shipment
  Email: alzstudy@iu.edu

## Slide 38
Fully cover the cryoboxes with about 2 inches of dry ice in the provided shipper.
Each Styrofoam shipper must contain about 45 lbs (20 kg) of dry ice.
Frozen Shipping – Dry Ice Requirements

## Slide 39
Dry Ice label should not be covered with other stickers and must be completed or the shipping carrier will reject/return your package!
Net weight of dry ice in kg
Frozen Shipping – Dry Ice Requirements
20.4

## Slide 40: UPS ShipExec System
Log into the ShipExec Thin Client at https://kits.iu.edu/ups
  If a new user or contact needs access, please reach out to your study contact for access
Follow instructions on section 8.2 of HEAD Manual of Procedures to create your return airbill and schedule a UPS pickup

## Slide 41: Shipping Regulations and Training
PLEASE NOTE:
All study personnel responsible for shipping should be certified in biospecimen shipping.
It is the responsibility of each site to ensure that the appropriate training has been provided and conducted in regards to IATA shipping.

## Slide 42
UN3373 Biological Substance, Category B Training
Biological Substance, Category B are specimens being transported for “investigational purposes”
Recommend: investigator sites document training of category B/dangerous goods
We recommend establishing a record of your staff’s training and date of instruction
The training records must be made available upon request by the appropriate national authority
  Additional information from the Department of Transportation (DOT) can be found on their website http://hazmat.dot.gov

## Slide 43: Biological Sample and Shipment Notification Forms
A copy of the sample form must be emailed to NCRAD prior to the date of sample arrival.
Please include sample forms in all shipments of frozen and ambient samples.
Email: alzstudy@iu.edu

## Slide 44: Biological Sample Notification Form- Baseline and 18M Visit
Send by E-mail and include a copy in each shipment
Blood collected for:
  Whole Blood for RNA
  Serum
  Plasma
  Buffy Coat/DNA
  Whole blood banking
  **Appendix B & C

## Slide 45: NCRAD Website Helpful Pages
NCRAD - Holiday Closures
NCRAD - Friday Blood Draws
Notes: UPDATE FOR SAMPLE TYPES?

## Slide 46: HEAD Active Study Page
NCRAD - HEAD Active Study Page
Notes: UPDATE PHOTO

## Slide 47: Contact Information
Questions?
Please contact NCRAD Coordinator at:
  Phone: 317-274-7890
  CRC email: dlkeys@iupui.edu
  Back-up email: alzstudy@iu.edu
  Website: www.ncrad.org